SPECIFIC OXYGEN UPTAKE RATE

Date:							Sample Location

Time							Analyst

Begin Temperature:			Average Temperature:			           End Temperature:

Oxygen Uptake Rate (OUR) (S.M.2710B)

OUR MG O2/L/hr = Begin Dissolved Oxygen – End Dissolved Oxygen X 60

Elapsed Time

OUR = (			mg/L -				mg/L) X 60     =			mg O2/L/hr

(	) Minutes

SOUR Total Solids TEST

Date  			   Time			      Operator Initials

Total Solids see S.M 2540G

Weight of Dish				A =

Weight of Dish and Sludge (Wet)		B=

Weight of Dish after drying		C=

% Solids =	(C - A)

(B - A)

% Solids   (			) – (			)    (		)

=		    =		*100  =

(			) – (			)    (		)

Specific Oxygen Uptake Rate (SOUR)

SOUR mg O2/hr/g =            OUR mgO2/L/hr

% Total Solids X 1000g/l

NOTE:  enter solids as a decimal

SOUR = (		) mg O2/L/hr  =					mg O2/hr/g

(		) x 1000 g/l

Temperature Adjustment

SOUR @ Average Temperature X correction factor = SOUR @ 20( C

MG O2/hr/g   X	  			MG O2/hr/g @20(C =

@		(C

Test Passes if Result < 1.5

Specific Oxygen Uptake Rate

Temperature Adjustment

SOUR is determined at the digester’s ambient temperature and then adjusted as follows.

SOUR@20°C = SOUR @ Ambient Temp. * A (20-Ambient temp.)

Where A = 1.05 above 20°

= 1.07 below 20°

These factors are good between 10° C and 30° C

Simplified

SOUR @20° C = SOUR @ Ambient Temp. * Correction

Correction = A (20-Ambient Temp)

Temp° C		Correction

10			1.97

11			1.84

12			1.72

13			1.60

14			1.50

15			1.40

16			1.31

17			1.22

18			1.14

19			1.07

20			1.00

21			0.95

22			0.90

23			0.86

24			0.82

25			0.78

26			0.75

27			0.71

28			0.68

29			0.64

30			0.61

# Text boxes

* 100