Sewer Rehabilitation Class	January and February 2007

Class Participation Notes

Module #1

WHAT ARE YOU CURRENTLY DOING TO ADDRESS INFLOW AND INFILTRATION SITUATIONS IN YOU COLLECTION SYSTEM?

Management Activities:

Begin CMOM Programs, Capacity-Management-Operations-Maintenance

Regulatory “Order” got the attention of Elected Officials

21 Year Effort to reduce I/I

Management emphasis to:

Build mains and service lines well

Rehabilitate Sewers

Reduce I/I

Address Stormwater Impacts

Remove Sump Pump contributions

Investigative Work: (listed by frequency of responses)

Flow Monitoring, some use permanently installed meters

TV Inspection

Smoke Testing,

Capacity Modeling

Visual Inspection

Pump Run Times

Overflow Monitoring

Flow Chasing, visually chasing flow from one manhole to another.

Dye Testing

Maintenance Activities:

Jet Cleaning

Service Line Service

Fats, oils, grease regulation

Emergency Repairs

Maintenance to reduce Overflows

Rehabilitation of existing sewer lines:

Cured-In-Place (CIP)

Bursting

Slip Lining

Point Repair/Point Repair

Line Replacement

Manhole Rehabilitation

Upsize Lines and pipes

Replace Gravity with Low Pressure

Upgrade Pump Stations

Remove Stormwater Connections

Repair Service Lines

Dig and Replace

Additional Capacity:

Construct Surge Basin or Equalization Basin at Plant

Expand Plant Capacity

Build New Plant

Module #2

BARRIERS OR OBSTACLES EFFECTIVE REHABILITATION

Poor Understanding of the Need

Education of Elected Officials and the Public

Attitudes the problem does not affect “Me”

Poor Ordinance Enforcement

Politics

Overwhelming Scope of the Task

Long-Term Neglect

System-Wide Problem

Unrealistic Expectation of Results

MONEY

Labor

Equipment

Other Utilities

Grant Requirements,

Disruption of Service

Existing Structures

Knoxville  Cost Per Foot of Sewer Line rehabilitation

Cured In Place (CIP)			$78

Pipe Bursting				$85

Digging & Replacement		$135

Plus Engineering/Inspection

Module #3

SEWER REHABILITAION PROGRAM GOALS

SHORT TERM GOALS

Achieve Zero Overflows

Reduce Inflow and Infiltration

Reduce Operating Costs

Gain Transmission or Treatment Capacity

LONG TERM GOALS

Meet a Regulatory Order

Improve Public Awareness

Reduce Overflows

Gain Capacity

Reduction in User Rates

Module #4

ACTION PLANS

SHORT TERM PLANS

Administrative Tasks				Operational Tasks

Budget Plans/ Requests			Smoke Test

Public Education				TV Lines

Analyze/Review Existing Data		Ground Inspection

Document Work Areas			Flow Monitoring/Checks

Trend Complaints & Repairs			Check Clean-Outs

Graph Data					Manhole Seals

Map System					Temperature Checks at Streams

INTERMEDIATE PLANS

Analyze Data for I/I Reduction from Past Projects

Funding Establishment

Intensify Construction Inspection

Reduce Overflows

Prepare for Growth